## Slide 1: Don’t care conditions
F(A,B,C,D)=Σm(4,12,13,14,15)+d(0,5,8)
AB
CD 00 01 11 10
00
01
A
11
C
10
B
D
AB
CD 00 01 11 10
00
01
A
11
C
10
B
D

## Slide 2: Multi-level NAND circuits
Convert all AND, OR gates to NAND gate symbols
Check all bubbles in the structure. For each bubble that is not counteracted by another bubble along the same line, insert a NOT gate or complement the input literal from its initial appearance.

## Slide 3: Lab 14
1. Implement a 4 bits BCD odd parity check circuit:
1.1 First consider the operating range of the BCD code.
1.2 When the number of 1’s are odd, the output is 0; otherwise, output is 1. Example:
input: 0001, output:0; input: 0101, output: 1.
2. Please implement it with the simplest Sum-of-Product form in Simulink only with NAND gates.
3. Test your circuit with 0101 and 0111.(use four constant wave generators)

## Slide 4: Today’s lab
Requirement:
Take the screenshot of the circuit structure in Simulink.
Take the screenshots of the scope wave when the inputs are set as 0101 and 0111.
If you don’t demonstrate the result to me in class, please submit it in canvas. I’ll create a portal later.