## Slide 1: Lab 9. Simplify the circuit
Combining Terms:
1. Combining terms. Use the theorem XY + XY’ = X to combine two terms. For example,
abc'd’ + abcd’ = abd’ [X = abd’, Y = c] (3-24)
When combining terms by this theorem, the two terms to be combined should contain exactly the same variables, and exactly one of the variables should appear complemented in one term and not in the other. Because X + X = X, a given term may be duplicated and combined with two or more other terms. For example,
ab'c + abc + a’bc = ab’c + abc + abc + a’bc = ac + bc

## Slide 2: Algebraic Simplification of Switching Expressions
Eliminating Terms and Literals:
2. Eliminating terms. Use the theorem X + XY = X to eliminate redundant terms if possible; then try to apply the consensus theorem (XY + X’Z + YZ = XY + X’Z) to eliminate any consensus terms. For example,
a'b + a‘bc = a‘b [X = a‘b]
a'bc’ + bcd + a’bd = a’bc’ + bcd [X = c, Y = bd, Z = a’b] (3-25)
3. Eliminating literals. Use the theorem X + X’Y = X + Y to eliminate redundant literals. Simple factoring may be necessary before the theorem is applied.

## Slide 3: Today’s lab
1. Simplify
The result have 3 terms, 4 literals.
2. Use Simulink to achieve the simplified function. Consider four inputs A, B, C, D. Please configure each pulse wave generator with different periods. Only one input port on the scope to show the output wave.
3. Please use Simulink to achieve the system shows in 1. Show the output is same as the result in 2.