## Slide 1
Applications of Boolean Algebra
Minterm and Maxterm Expansions
Unit 4

## Slide 2
This chapter includes:
4.1 Conversion of English Sentences to Boolean Equations
4.2 Combinational Logic Design
Using a Truth Table
4.3 Minterm and Maxterm Expansions
4.4 General Minterm and Maxterm Expansions
4.5 Incompletely Specified Functions
4.6 Examples of Truth Table Construction
4.7 Design of Binary Adders and Subtracters

## Slide 3: Combinational Logic Design Using a Truth Table
Logic Design with Truth Tables:
Take a three-input, one output system where A,B,C are inputs that represent the digits of binary number N and f is the output such that f=1 if N>=3 and f=0 if N<3.

## Slide 5: Combinational Logic Design Using a Truth Table
Logic Design with Truth Tables:
OR-ing the terms that yield value 1 will result in
f=AB’C+ABC’+ABC
Where the expression equals 1 if A,B, and C take on any of the three combinations of values 101, 110 or 111.

## Slide 6: Standard forms
Standard forms are standard ways to express Boolean functions
They contain product terms (Minterms) and sum terms (Maxterms)
They result in more desirable expression for circuit implementation
Minterms are AND terms with every variable present in either true or complement form
Maxterms are OR terms with every variable present in either true or complement form

## Slide 7: Minterm
A function with n variables has 2n minterms. The literals are listed in the same order for all minterms (usually alphabetically)

## Slide 8: Minterm
A variable in a minterm is complemented for 0 and is not complemented for 1

## Slide 9: Sum of minterms canonical form
Function expressed as a logical sum (OR) of minterms
Sum of all minterms where the function value is 1

## Slide 10: Maxterm
A function with n variables has 2n maxterms. The literals are listed in the same order as for the maxterms with a corresponding maxterm

## Slide 11: Maxterm
A variable in a maxterm is complemented for 1 and is not complemented for 0

## Slide 12: Product of maxterms canonical form
Function expressed as a logical product (AND) of maxterms
Product of all maxterms where the function value is 0

## Slide 13: Minterms and maxterms relationship
DeMorgan’s Theorem
Two variable example:

## Slide 14: Function complements
The complement of a function expressed as a sum of minterms is constructed by selecting the minterms missing in the expression
Alternatively, the complement of a function expressed as a sum of minterms is simply the product of maxterms with the same indices

## Slide 15: Function complement example

## Slide 16: Sum-of-Products (SOP)

## Slide 17: Sum-of-Products (SOP) example

## Slide 18: Product-of-Sums (POS)

## Slide 19: Cost criteria

## Slide 20: Input costs

## Slide 21: Design of Binary Adders and Subtracters
Full Adder Truth Table: