## Slide 1
Three-state buffer, Encoder, Decoders, Multiplexers, Demultiplexers
Unit 9 II

## Slide 2: Multiplexers
A multiplexer selects information from one of many input lines and directs it to an output line
I0 I1 I2 I3
S1 S0
Y
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3

## Slide 3: Multiplexers

## Slide 4: Multiplexers
A multiplexer can be implemented using a decoder, 2-input AND gates and multiple-input OR gate:

## Slide 5
Decoder + multiplexer/demultiplexer application

## Slide 6: Cascading Multiplexers
8-to-1-line multiplexer
I0 I1 I2 I3
I
4
I5 I6 I7
S1 S0
Y
S2
0 | 4-to-1- Line MUX |  | 
1 |  |  | Y
2 |  |  | 
3 | S1 | S0 | 
0
4-to-1-
Line
MUX
Y
1
2
3
S1 S0
0
2-to-1-Line
Y
1
MUX
S

## Slide 7: Demultiplexers
A Demultiplexer directs the information from a single input line to one of 2n output lines and is controlled by n control lines
Example – 1-to-4-line demultiplexer:
Y0 Y1 Y2 Y3
S1 S0
I
S1 | S0 | Y0 | Y1 | Y2 | Y3
0 | 0 | I | 0 | 0 | 0
0 | 1 | 0 | I | 0 | 0
1 | 0 | 0 | 0 | I | 0
1 | 1 | 0 | 0 | 0 | I

## Slide 8: Old ways of implementing digital circuit
Using the fundamental gates NAND gate and NOR gate, different functions can
be achieved.
Resistors, triodes and capacitors are utilized but can only implement a fixed single
function.

## Slide 9: Programmable Logic Devices
Programmable Array Logic (PAL):
The PAL (programmable array logic) is a special case of the programmable logic array in which the AND array is programmable and the OR array is fixed
PAL has same structure as PLA in Figure 9-28.

## Slide 10: Programmable Logic Devices

## Slide 11: Field Programmable Gate Array(FPGA)

## Slide 12: What is Software Defined Radio?
An SDR is a FPGA-based reconfigurable computing platform in which most of the radio functionality is implemented in software.
While traditional hardware-based radios are designed for one or a small number of applications.
Therefore, SDR systems lie at the intersection between RF electronics, embedded computing, and digital signal processing.

## Slide 13: SDR Transceivers

## Slide 14: RTL-SDR
RTL-SDR is a USB device to receive the RF radio signals. By tuning the receiving frequency, it is capable to demodulate the received signal.