## Slide 1: Review for midterm

## Slide 2: Key points
Number conversion
2’s complement
Addition, subtract, overflow
Boolean expressions.
Draw circuit diagram using Boolean expressions
Simplification theorems
Prove the validity
Truth table
Exclusive OR
Sum-of-Product and minterms
Use Boolean expression to specify a system
Use K-map to simplify the Boolean expressions

## Slide 3
Convert -100 from base-10 to hexadecimal(16 bits two’s complement notation).
Number conversion & 2’s complement

## Slide 4
Convert -100 from base-10 to hexadecimal(16 bits two’s complement notation).
Number conversion & 2’s complement

## Slide 5
Addition, subtract, overflow
Use 7 bits 2’s complement to represent the following numbers and compute the result,
determine if there’s an overflow.
-14-32.

## Slide 6
Addition, subtract, overflow
Use 7 bits 2’s complement to represent the following numbers and compute the result,
determine if there’s an overflow.
-14-32.

## Slide 7
Logic gates and circuit diagram
Draw the circuit diagram of F(A,B,C)=A’B+B’C using the AND, OR and NOT gates.

## Slide 8: Algebraic Simplification Procedures
Combining Terms:
1. Combining terms. Use the theorem XY + XY’ = X to combine two terms. For example,
abc'd’ + abcd’ = abd’ [X = abd’, Y = c] (3-24)
When combining terms by this theorem, the two terms to be combined should contain exactly the same variables, and exactly one of the variables should appear complemented in one term and not in the other. Because X + X = X, a given term may be duplicated and combined with two or more other terms. For example,
ab'c + abc + a’bc = ab’c + abc + abc + a’bc = ac + bc

## Slide 9: Algebraic Simplification Procedures
Eliminating Terms and Literals:
2. Eliminating terms. Use the theorem X + XY = X to eliminate redundant terms if possible; then try to apply the consensus theorem (XY + X’Z + YZ = XY + X’Z) to eliminate any consensus terms. For example,
a'b + a‘bc = a‘b [X = a‘b]
a'bc’ + bcd + a’bd = a’bc’ + bcd [X = c, Y = bd, Z = a’b] (3-25)
3. Eliminating literals. Use the theorem X + X’Y = X + Y to eliminate redundant literals. Simple factoring may be necessary before the theorem is applied.

## Slide 10
Simplify the circuit: F(A,B,C)=ABC+A’BC+AB’C. The results only have three literals.
Simplification theorems

## Slide 11
Prove the validity & XOR
Is the following distributive law valid? A⊕BC=(A⊕B)(A⊕C)

## Slide 12
Simplification theorems
Reduce to a minimum sum of products(answer only has two literals):
Y(X’+Z’)+(XY+Y’Z)

## Slide 13
Simplification theorems
Reduce to a minimum sum of products:
(A+B)(C⊕D)+AB’

## Slide 14
There are three input signals A, B, C. If three inputs are 0 at the same time
or only two signals are 1 at the same time, the output F is 1, otherwise, F is 0.
Build its truth table
Truth table & Use Boolean expression to specify a system

## Slide 15
Sum-of-Product and minterms
Given F(A,B,C)=A’BC’+C.
Express F as a minterm expansion.

## Slide 16: Determination of Minimum Expressions Using Essential Prime Implicants
Procedure to Obtain a Minimum Sum of Products from a Karnaugh Map:
Find all prime implicants
Include all essential prime implicants
Include other prime implicants to cover all minterms not yet covered. Try to minimize the overlap between the prime implicants

## Slide 17
Use K-map to simplify the Boolean expressions
Use K-map to simplify the following functions:
F(A,B,C)= Σm(0,4,5,6,7)
F(A,B,C)=Σm(0,2,3,7)

## Slide 18
Use K-map to simplify the Boolean expressions
AB
CD 00 01 11 10
1 | 0 | 1 | 1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
1 | 1 | 1 | 1
00
01
A
11
C
10
B
D
AB
CD 00 01 11 10
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 0 | 0 | 1
00
01
A
11
C
10
B
D