## Slide 1: Introduction to Computer Organization

## Slide 2: Simple Computer Architecture
1.Datapath, which consists of:
A set of registers
The micro-operations performed on data stored in the registers
The control interface
2. Control Unit, which provides signals that control micro-operations performed in the Datapath and other components
In computer systems, a shared arithmetic/logic unit (ALU) is used to perform micro-operations
The contents of registers are transferred to the ALU, which performs the operation and then transfers them to the destination

## Slide 3: Datapath

## Slide 4: Denotation of the registers
Registers are denoted by uppercase letters (followed by numbers)
The individual flip-flops in a n bit register are numbered from 0 to n-1 with 0 the LSB

## Slide 5: Denotation of data transfer
Data transfer from one register to another is denoted using the ← operator
R2 ← R1
R1 is the source of transfer and R2 the destination
Conditional statements used when data transfer occurs only on receiving a control signal
K1: R2 ← R1
K1 can be any Boolean function or variable that evaluates to 0 or 1
K3: R2 ← R1, R1← R2

## Slide 6: Datapath
To perform R1 ← R2 + R3
The control unit must provide the following control inputs:
A select, to place contents of R2 onto A data and Bus A
B select to place contents of R3 onto 0 input of MUX B; and MB select to put 0 input of MUX B onto Bus B
G select, to complete A+B
MF select, to place the ALU
output on the MUX F output
MD select, to place the MUX F output onto Bus D
Destination select, to select R1 as the destination of the data on Bus D
Load enable, to enable R1 to be loaded

## Slide 7: Arithmetic/Logic unit
An arithmetic/logic unit (ALU) is a combinational circuit that performs basic arithmetic and logic operations

## Slide 8: Arithmetic/Logic unit
Performs a set of basic arithmetic and logic micro-operations
The n-bit result is output on vector G with carry-out on Cout
S2 selects between arithmetic or logic operations S1 and S0 select one of 4 operations within the arithmetic or logic operations
Can be extended to 8 operations by using the Cin(carry-in) input

## Slide 9: Arithmetic unit

## Slide 10: Arithmetic unit
The arithmetic circuit is based on the n-bit parallel adder
By controlling the inputs to the adder, different types of arithmetic operations can be obtained
Connect the X input of the adder directly to operand A Make the input Y some function of operand B

## Slide 11: Arithmetic unit
Use a truth table and k-maps to implement the select logic on input B

## Slide 12: Arithmetic unit

## Slide 13: Logic unit
Performs bitwise logical operations on the bits of the operands
There are four commonly used logic operations- AND, OR, XOR, and NOT
One stage logic unit: (as many as n-bit are required)
S1 | S0 | Output | Operation
0 | 0 | G = A & B | AND
0 | 1 | G = A ¦ B | OR
1 | 0 | G = A  B | XOR
1 | 1 | G = A' | NOT

## Slide 14: Arithmetic/Logic unit

## Slide 15: Arithmetic/ Logic unit

## Slide 16: The Shifter
The shifter shifts the value on Bus B by one bit to the left or by one bit to the right
Constructed using a combinational circuit so not dependent on the system clock
The shifter can be designed using n multiplexers with two select lines:
S = 00 – no shift
S = 01 – right shift
S = 10 – left shift

## Slide 17: The Shifter