## Slide 1
Introduction
Unit 1

## Slide 2: Learning Objectives
Introduction:
Explain the difference between analog and digital systems, as well as why digital systems are capable of greater accuracy
Understand the difference between combinational and sequential circuits
Explain why two-valued signals and binary numbers are commonly used in digital systems

## Slide 3: Digital Systems and Switching Circuits
Digital and Analog Systems:
In a digital system, physical quantities can only assume discrete values.
In an analog system, physical quantities or signals can vary continuously over a specified range.

## Slide 4: Digital systems
Take the discrete values as the inputs, it can generate discrete outputs.
Examples: vending machine
Why we widely use digital systems?

## Slide 5: Digital Systems and Switching Circuits
Design of digital systems:
System design: breaking the overall system into subsystems and specifying the characteristics of each subsystem.
Logic design: determining how to interconnect basic logic building blocks to perform a specific function.
Circuit design: specifying the interconnection of specific hardware components to form a gate, flip-flop or other logic building block.

## Slide 6: Digital Systems and Switching Circuits
Switching circuits: a switching circuit has one or more inputs and one or more outputs which take on discrete values.
In combinational circuits, output values of circuit only depend on the present values of inputs, not past.
In sequential circuits, output values of circuit depend on both past and present input values. For this reason, sequential circuits are said to have “memory”, because they must remember past sequence of inputs.

## Slide 7: Digital Systems and Switching Circuits

## Slide 8: Summary
1. combinational circuits:
don’t consider the system states
2. sequential circuits
Synchronous circuits
system states update only at specific time
Asynchronous circuits
system states update at any time as an event is triggered

## Slide 9
0 | 0 | 1 | 3 | 5 | 6 | 4
Digital Counter
Count Up
Reset
Inputs: Outputs:
State:
Example
Synchronous circuits or Asynchronous circuits?

## Slide 10: Digital Systems and Switching Circuits
Building Blocks of Switching Circuits:
Basic building block of combinational circuits: logic gate
Basic building block of sequential circuits: flip-flop
Switching devices used in digital systems are usually two-state devices, meaning the output can only assume one of two discrete values.
Because the outputs of most switching devices assume only two different values, it is natural to use binary numbers internally in digital systems.

## Slide 11: Binary value representation
Digital signal
Boolean
Switch
Voltage

## Slide 12
Time
Continuous or Discrete? Synchronous or Asynchronous?

## Slide 13: Quantization

## Slide 14: Content expansion: Is CPU asynchronous or synchronous sequential circuit?

## Slide 15
Content expansion: Is human being’s behavior asynchronous or synchronous?

## Slide 16: Humanoid Robots
https://www.youtube.com/watch?v=VsbgCPOW1HQ

## Slide 18: How to design the robot?
Act immediately
Act after thinking
Combinational Circuit
Sequential Circuit